## Slide 1: DaniS506 / DaniATAPI / DaniBoot
High-Performance Serial/Parallel ATA/ATAPI drivers (and more) Updates and Outlook Daniela Engert

## Slide 2: What are the »Dani« drivers?
DaniS506.ADD Replacement for IBM1S506
DaniATAPI.FLT Replacement for IBMIDECD and IBMATAPI
DaniBoot.FLT Replacement for CD_BOOT

## Slide 3: DaniS506

## Slide 4: DaniS506 Basics
S506 is the first »small form factor disk« interface standard
The standard is modelled after the registers found in the WD1003 MFM disk controller
In the '80s, the controller moved into the disk drive (thus IDE = »Integrated Drives Electronic«), and the physical disk interface became an extension of the ISA bus
This interface is known as »ATA«

## Slide 5: DaniS506 Basics
The ATA interface became became formally standardized by the ANSI T13 committee
Over time, a heap of new features was added, the ATA physical interface was decoupled from the system IO bus, the interface speed increased 30 fold, and increasingly sophisticated CPU offloading schemes were introduced
The current ATA/ATAPI standard is version 6

## Slide 6: DaniS506 Basics
Eventually, ATA disks became »storage appliances with a funny interface«, running a full-fledged OS inside - just like SCSI disks
The evolution of both the ATA host and disk side gave way to implement protocols and command sets beyond ATA - the invention of ATAPI
Today, an ATA channel is a bus which »speaks« two languages: ATA and SCSI

## Slide 7: DaniS506 Basics
Both ATA/ATAPI and SCSI share the same problems:
Parallel interfaces run against the »speed wall« at the physical layer
Buses are shared transport channels, the transport capacity has to be split between all attached units
Compatibility to first generation hardware eats up large portions of the bandwidth

## Slide 8: DaniS506 Basics
Parallel ATA is DEAD!
(and so is parallel SCSI, too)

## Slide 9: DaniS506 SATA
The solution to PATA is »serial ATA« (SATA)
serial physical signalling -> no speed limit
7 wires instead of 80 wires -> reliable
point-to-point only -> defined conditions
switched networking -> no bus contention
hotplug interface -> no maintenance down time

## Slide 10: DaniS506 »Ecosystem«
All but full coverage of the PATA and SATA controller market (w.r.t. OS/2) in a single driver:
17 chip manufacturers (all majors)
113 PATA controller chips
26 SATA controller chips
plus: OEM variants, chipset variants

## Slide 11: DaniS506 Chip Support
The driver supports even »unsupported« (i.e. unknown) chips as long as the controller implementation matches the ANSI T13 committee interface specification
The driver autodetects such controllers if the user enables this feature
The companion DUMPIDE utility detects the presence of such controllers even without loading the driver.

## Slide 12: DaniS506 Chip Support
The driver
supports both desktop and server machines
supports PCI classic, PCI-X and PCI-express
supports virtually all currently known or announced products
supports the maximum performance on all products
works around known chip defects where possible

## Slide 13: DaniS506 Automation Features
Operation »out of the box« on virtually all machines
Autodetection of the ATA channel configuration (f.e. wiring) unless the manufacturer »forgot« to implement means to do so
Autoconfiguration of the ATA channel setup (f.e. communication speed) according to the capabilities of the involved components

## Slide 14: DaniS506 benefits
A single OS/2 installation image may be deployed on all systems with PATA and/or SATA controllers
In virtually all cases the driver defaults to both reliable operation and best performance
Usually, option flags are required only to address »special« requirements.

## Slide 15: DaniS506 Convenience Features
Users may trade communication speed with data transfer reliability
Users may trade disk access times with disk noise
Users may trade disk access latency with disk power consumption

## Slide 16: DaniS506 SATA Features
In addition to the feature set found with PATA units, the driver supports on SATA:
PATA-to-SATA bridges
device hot-plugging
  external units
  swappable disk enclosures
full support of SATAPI (if the controller implements this protocol)

## Slide 17: DaniS506 and RAID
None of the supported controllers have any RAID support features worth mentioning, even if these controllers are marketed as RAID controllers
Their RAID is implemented by software only
All of these software RAIDs use vendor specific disk layouts
DaniS506 does not implement any of these RAID schemes

## Slide 18: DaniS506 Status
Current version is 1.7.0
Driver is considered as »production safe«
There are no known driver defects
The driver applies all known fixes to enable a successful OS/2 boot:
  VIA PCI arbiter bug
  AMD/NVidia prefetch bugs
  NVidia Processor disconnect hang

## Slide 19: DaniS506 Outlook
New controller chips are added continuously Problem: chip documentation is sparse (at best)
The ATA transport layer is currently in rework to support controllers which don't follow the T13 interface standard:
  AHCI SATA-2 standard (Intel, SiS, ...)
  Promise PDC203xx/206xx chips
  Marvell 4/8-port SATA chips

## Slide 20: DaniS506 Outlook
The DaniS506 source code is slowly converging with the DaniATAPI source code sharing increasingly larger portions of the code
Eventually DaniS506 and DaniATAPI will merge into a single driver, possibly named
DaniATA

## Slide 21: ATA RAID Outlook
There are true hardware RAID controllers with PATA or SATA interfaces available
Drivers for the well-adopted 3Ware (now AMCC) Escalade 4 to 12 port controllers are in the making - stay tuned!

## Slide 22: DaniATAPI

## Slide 23: DaniATAPI Basics
Question: What is »ATAPI« ?
Answer: SCSI in »disguise« ! ATAPI has been invented as means to implement the SCSI command set and protocol suite on the ATA channel, which supports by design - and heritage - a disk-only transport protocol.

## Slide 24: DaniATAPI Device Support
The driver supports basically all ATAPI devices:
Removable media disks (ZIP, Jazz, etc.)
CD/DVD readers and writers
Magneto-optical units
WORMs
Optical phasechangers (PD-units)
Combinations of the above in combo units

## Slide 25: DaniATAPI benefits
One single driver for all ATAPI device classes
Controller-specific workarounds for deviations from the standard controller programming model enable DMA mode operation on most controllers
ATAPI devices may be transparently treated like SCSI devices. DaniATAPI has a fully implemented SCSI software interface!

## Slide 26: DaniATAPI Status
Current version is 0.3.18
Driver is considered »production safe«
There are no known driver defects

## Slide 27: DaniATAPI Outlook
At present there is no major development planned on the current code basis
Wherever possible common source modules are shared with DaniS506
Driver is going to be merged with DaniS506 to open the road to future enhancements: better performance, better hotplug support

## Slide 28: DaniBoot

## Slide 29: DaniBoot Basics
The OS/2 boot process and the OS/2 driver architecture supports booting off media only, if they become visible to the DASD layer in the first boot stage; but support for ISO9660 or UDF formatted CDs/DVDs becomes available in later stages
DaniBoot (and IBM's CD_BOOT) present a »DASD view« of bootable CDs and DVDs

## Slide 30: DaniBoot Features
The driver
works on systems with more than one CD or DVD unit
gives much better performance on most systems
supports multiple bootable OS on a single CD or DVD (f.e. OS/2, Windows and Linux)
is much easier to use when creating bootable OS/2 CDs

## Slide 31: DaniBoot Status
Current version is 1.0.2
Driver is considered »production safe«
No known driver defects

## Slide 32: DaniBoot Outlook
Driver is »stable«
At present there are no plans for additional features