## Slide 1: OS/2 Device Driver Support / USB 2.0
Modris Berzonis
(modrisb@exigengroup.lv)

## Slide 2: Summary
Updated driver packages
USB & OS/2
Stack design
Supported client/class drivers
Supported host controller drivers
APM & driver stack
USB 2.0 support
Class driver extensions?
Driver Code sizes

## Slide 3: Updated Driver Packages
Intel Gigabit Ethernet driver
UDF 2.0
IDEDASD
Large hard disk support (512GB)
SingleMouse

## Slide 4: Intel Gigabit Ethernet
New chipsets added - 82541GI/82543GC
More flexible parameter processing
TCP/IP & NETBIOS coexistence
Suspend/resume support
Performance reached up to 57 MBps by varying
  transmit/receive buffer counts (8-255)
  Frame size (regular/jumbo)
  MTU value
  Disk operation mode (avoid PIO)
Debug version

## Slide 5: UDF 2.01
Suspend/resume support
  IFS stops sending I/O requests to device(s) after suspend notifications
  IFS does not send I/O requests to device(s) before device has not completed resume activities
Mt.Rainier support
Format extensions – verification support
Performance improvements
  6 X 64KB cache buffers
  Write on sorted LBA
  Enhanced buffer flush procedure

## Slide 6: UDF 2.01
Features to come
  Defect management for CD-RW / DVD+/-RW
  New format modes:
    Erasing
    Wait for background format completion
    Support of 3 different UDF revision formats
    Logical format performance increase
    Background format suspend for CD-MRW
    Logical format bypassing

## Slide 7: IDEDASD
ICH6 support
SMART command support
  Developer information will be published
Resume code enhancement
Extended detection update

## Slide 8: Large Hard Disk Support (512GB)
Sector per track count increase
Fixed cylinder count calculation algorithm
Limited boot support – disk size up to 512GB
Data disk size up to 2TB
Updates in OS2LVM.DMD/ OS2DASD.DMD/ LVM.DLL/ UHPFS.DLL

## Slide 9: SingleMouse
Problem fixes for systems without USB mouse installed

## Slide 10: OS/2 & USB
Started development in 1997
Limited driver support for USB 1.0/1.1
Added USB 2.0 support in 2002

## Slide 11
Stack Design
Class Driver
Class Driver
Class Driver
USBD
EHCI Host Driver
UHCI Host Driver
OHCI Host Driver
OS/2 Interface

## Slide 12: Supported Client/Class Drivers
Ethernet – only vendor specific interface
  Kawasaki KL5KUSB101 chipset
  MPTS controlled vendor/device IDs
Serial converter
  3 different vendor specific interfaces
    1 - Future Technology Devices International FT8U100AX chip
    2 - Belkin F5U103
    3 – MCT (Magic Control Technology) USB to RS232 converter
  vendor/device ID specification through CONFIG.SYS parameters :USBSer.sys [/V] [/IDV:hhhh /IDP:hhhh /TYPE:d]

## Slide 13: Supported Client/Class Drivers
Modem
  ACM (abstract control model / AT command mode)
Quatech USB to serial converters
Mass Storage devices
  Support for hard disk class (floppy drives / removables / hard disks); CDROM class and Optical device class
  Works with predefined number of devices in each class, like: /FLOPPIES:i /REMOVABLES:j /FIXED_DISKS:k /CDS:l /OPTICALS:m
  Predefined floppy size list, includes LS120/LS240 devices
  Multi-LUN device support
  Device status monitor support

## Slide 14: Supported Client/Class Drivers
Mass Storage devices
  Port reset feature
Printers
  Request cancellation with status return

## Slide 15: APM & driver stack
Controlled through USBD driver
Implementation for MSD class driver
  Switching off motor during suspend event processing

## Slide 16: Supported Host Controller Drivers
UHCI
  Only USB v1.0/1.1
  Companion controller for EHCI
OHCI
  Only USB v1.0/1.1
  Possible companion controller for EHCI
EHCI
  Only USB v2.0
  Requires companion controller(s) to support 1.0/1.1 devices

## Slide 17: USB 2.0 support
New host controller driver
Minimal changes in USBD/Class drivers
MSD driver extension to support larger data buffers

## Slide 18: Class/Host Driver Extensions?
Communication Class
  Extended modem support
  Ethernet support
  ISDN modem support
MSD
  Optical device support
IrDA bridge
Imaging
Cardbus USB host support

## Slide 19: Driver Code Sizes
Host Controller drivers
  UHCI 10 Kloc
  OHCI 11 Kloc
  EHCI 14 Kloc
USBD driver 6 Kloc
Keyboard 2.5 Kloc
Mouse 4 Kloc
Ethernet 5 Kloc
HID 3 Kloc
Serial 6 Kloc
Audio 12 Kloc
MSD 11 Kloc